## Slide 1
Sun-Earth L₂ Point Nulling Interferometry Formation Flying Performance Analysis
Aiden Weatherbee MSc Student, Astronautics and Robotics Laboratory (ASTRO Lab), Department of Physics & Astronomy, York University, Email: aidenweatherbee@hotmail.com
Sarah Rugheimer
Associate Professor, Department of Physics & Astronomy, York University; Reader, University of Edinburgh
Email: srughei@ed.ac.uk
Michael C.F. Bazzocchi
Associate Professor, Astronautics and Robotics Laboratory (ASTRO Lab), Department of Earth & Space Science & Engineering, York University, Email: mbazz@yorku.ca
Astrodynamics Specialist Conference 2026, Whistler, BC
AAS 26-967
Notes: HI everyone, my name is aiden Weatherbee. Today ill be talking about a 144 case trade study for a formation flying nulling interferometer concept at the sun-earth l2 point.

## Slide 2
The Goal: Characterize Terrestrial Worlds with LIFE
(Credit: Meadows and Crisp, 1996; Tinetti et al., 2005; Tinetti et al., 2006; Kaltenegger et al., 2007; Selsis et al., 2007b)
Wavelength covers peak emission of Earth-like exoplanets
Features absorption bands of O3, CH4, N2O
Thermal emission carries atmospheric information
Introduction
Background
Problem
Methodology
Results
Conclusion
Notes: So to start off im going to give you an introduction to why nulling interferometry is appealing. A central concern of modern astrophysics is to directly image temperate terrestrial worlds. The LIFE mission- which stands for Large Interferometer For Exoplanets- is a formation flying nulling interferometer concept that aims to do this by the 2040’s. A key reason that this mission is wanted by the community is that it can null the starlight to access the planets mid infrared thermal emission , which contains key habitability indicators of interest such as ozone, methane, and nitrous oxide

## Slide 3
For a nulling interferometer (e.g., LIFE) there are several mission level design variables that affect the design of both the formation control and the optics.
We study the relative formation error and fuel usage of these key variables.
Formation control and optical control must be co-designed: formation errors couple directly into nulling and modulation errors.
Introduction
Background
Problem
Methodology
Results
Conclusion

## Slide 4
Past Concepts:
TPFI (credit: NASA)
https://www.astro.princeton.edu/~dns/FRS120/RFI/134_TPF-I_Lawson_EOS.pdf
DARWIN (credit: ESA)
Formation Flying:https://www.esa.int/ESA_Multimedia/Images/2015/06/Darwin_s_six_telescopes
https://www.esa.int/Enabling_Support/Space_Engineering_Technology/Proba-3
Introduction
Background
Problem
Methodology
Results
Conclusion
https://slab.stanford.edu/projects/stari
https://science.nasa.gov/mission/grace-fo/
4
Notes: For a bit of context, LIFE is actually inspired by past nulling interferometer concepts- NASA’S TPFI and ESA’S DARWIN. These missions were cancelled due to unknown mission yields, which has since been answered, and immature formation flying

## Slide 5
Past Concepts:
TPFI (credit: NASA)
https://www.astro.princeton.edu/~dns/FRS120/RFI/134_TPF-I_Lawson_EOS.pdf
DARWIN (credit: ESA)
Formation Flying:https://www.esa.int/ESA_Multimedia/Images/2015/06/Darwin_s_six_telescopes
Past/Future Tech Demos:
Proba-3 (credit: ESA)
https://www.esa.int/Enabling_Support/Space_Engineering_Technology/Proba-3
STARI (credit: Stanford SRL)
GRACE-FO (credit: NASA)
4
Introduction
Background
Problem
Methodology
Results
Conclusion
https://slab.stanford.edu/projects/stari
https://science.nasa.gov/mission/grace-fo/
Notes: There have since been several missions that have tackled the formation flying issue such as proba 3 and grace-fo.

## Slide 6
Past Concepts:
TPFI (credit: NASA)
https://www.astro.princeton.edu/~dns/FRS120/RFI/134_TPF-I_Lawson_EOS.pdf
DARWIN (credit: ESA)
Formation Flying:https://www.esa.int/ESA_Multimedia/Images/2015/06/Darwin_s_six_telescopes
Past/Future Tech Demos:
Proba-3 (credit: ESA)
https://www.esa.int/Enabling_Support/Space_Engineering_Technology/Proba-3
STARI (credit: Stanford SRL)
GRACE-FO (credit: NASA)
Inspiration in this Study:
In-plane vs Out-of-plane (TPFI vs Darwin)
12,18, 24 hour rotation rates (TPFI vs LIFE vs Darwin)
45, 65, 85 degree pointing angle (TPFI/LIFE/Darwin inspired)
Sensors inspired by Proba-3, GRACE-FO, and STARI
4
Introduction
Background
Problem
Methodology
Results
Conclusion
https://slab.stanford.edu/projects/stari
https://science.nasa.gov/mission/grace-fo/
Notes: All of these missions have inspired this trade study through the trade variables and sensor models.

## Slide 7
Telescope 2
Telescope 4
Combiner
Telescope 1
Telescope 3
Planet
Star
Introduction
Background
Problem
Methodology
Results
Conclusion
Nulling Interferometry
Notes: Before I go any farther into my trade study, I want you to understand how nulling interferometry works so you can understand the results. So the fundamental idea is that you can take multiple mirrors on separate spacecraft and combine the light inside a separate combiner spacecraft. This allows you to achieve the resolution needed to distinguish the star from the planet in the mid infrared wavelengths. Think of it like taking jwst’s hexagonal segments and separating them to increase its resolution.

## Slide 8
Telescope 2
Telescope 4
x2
Combiner
Telescope 1
Telescope 3
Planet
Star
Introduction
Background
Problem
Methodology
Results
Conclusion
Nulling Interferometry
Notes: The formation is expected to stay close to ridged, so the combiner spacecraft then has controllable optics that corrects for errors in formation control that cause tip/tilt and optical path difference errors. In the light beam.
This is then injected into fibre optic cables where a pi phase shift is applied, and the beams are combined. The pi phase shift is what causes the nulling of the star.

## Slide 9
Telescope 2
Telescope 4
x2
Combiner
Telescope 1
Telescope 3
Planet
Star
Introduction
Background
Problem
Methodology
Results
Conclusion
Nulling Interferometry
Notes: You then rotate the array to modulate the planets signal through the dark and light fringes, while the on axis star remains destructively interfered in the dark fringe.

## Slide 10
D. Rouan
Imaging Interferometer
Combiner Spacecraft
Star
Planet
Introduction
Background
Problem
Methodology
Results
Conclusion
Notes: A key thing I want to highlight is that the nulling of the star relies on the ability to control the optical beam to within a pi phase shift of light. This is what distinguishes a nulling interferometer from an imaging interferometer.

## Slide 11
Combiner Spacecraft
Pi Phase Inversion
Nulling Interferometer
Star
Planet
D. Rouan
Introduction
Background
Problem
Methodology
Results
Conclusion
Notes: The achromatic pi phase shift is what holds the dark fringe. The star is expected to be on the order of 1 billion times brighter than the planet, so even a small break in this control can completely overwhelm the planets signal.

## Slide 12
Optical Path Difference / Phase Mismatch
Introduction
Background
Problem
Methodology
Results
Conclusion
Notes: This makes holding the optical path difference the central concern of nulling interferometry. This figure shows how a 1 mm error along LOS can result in a roughly 2 mm OPD error, which corresponds to 200 wavelengths of light at 10 micrometers.

## Slide 13
Optical Path Difference / Phase Mismatch
Planet Modulation Error
Introduction
Background
Problem
Methodology
Results
Conclusion
Notes: Cross LOS errors can also cause Planet Modulation errors, which shifts the exoplanets signal within the spectrum, making it harder to detect from background noise. Really the point of this is to show that the formation control system is directly coupled to the optical control system, directly affecting the scientific yield.

## Slide 14
2 x Controller
PD vs CR3BP-LQI
8
Introduction
Background
Problem
Methodology
Results
Conclusion
144 Case Trade Study Variables
Notes: That brings us to this trade study. As mentioned, this is a 144 case trade study that varies key mission level design choices that affect both the optical control system and the formation and attitude control systems. So we test 2 difference controllers- a simple PD , and a cr3bp based linear quadratic integrator.

## Slide 15
2 x Combiner placement
In-plane combiner vs out-of-plane combiner
2 x Controller
PD vs CR3BP-LQI
8
Introduction
Background
Problem
Methodology
Results
Conclusion
144 Case Trade Study Variables
Notes: WE test the 2 different chief placements that Life is considering, inspired by TPFI and Darwin, which is in plane vs out of plane shown on the side there

## Slide 16
2 x Combiner placement
In-plane combiner vs out-of-plane combiner
3 x Array rotation
12 h, 18 h, 24 h array-rotation periods
2 x Controller
PD vs CR3BP-LQI
8
Introduction
Background
Problem
Methodology
Results
Conclusion
144 Case Trade Study Variables
Notes: We test the 3 array rotation periods of again TPFI, LIFE, and DARWIN

## Slide 17
2 x Combiner placement
In-plane combiner vs out-of-plane combiner
3 x Array rotation
12 h, 18 h, 24 h array-rotation periods
3 x Pointing angle
45°, 65°, 85° line-of-sight cases
2 x Controller
PD vs CR3BP-LQI
8
Introduction
Background
Problem
Methodology
Results
Conclusion
144 Case Trade Study Variables
Notes: And then to ensure these results are robust over the expected array orientations, we test across the range of viable viewing angles with 45 degrees, 65 degrees, and 85 degrees with respect to the sun-earth line.

## Slide 18
2 x Combiner placement
In-plane combiner vs out-of-plane combiner
3 x Array rotation
12 h, 18 h, 24 h array-rotation periods
3 x Pointing angle
45°, 65°, 85° line-of-sight cases
2 x Controller
PD vs CR3BP-LQI
4 x Combiner orbit
JWST-like halo; small periodic halo; quasi-halo; Lissajous-family trajectory
8
Introduction
Background
Problem
Methodology
Results
Conclusion
8
144 Case Trade Study Variables
Notes: This is also tested across 4 different L2 orbit types, as L2 is a quite chaotic regime, these 4 orbit types were chosen as a representative wide spread of initial orbit conditions to ensure the results remain robust.
Everything else remains fixed, and this gives us the 144 cases.

## Slide 19
Follower Spacecraft Control System
Attitude Estimation
-MRP square root UKF
Attitude Control
-MRP PD feedback
Position Estimation
-CR3BP nonlinear square root EKF
Position Control
-CR3BP LQI
or
-PD
Attitude Sensors
-Star tracker
-IMU
Position Sensors
-Laser metrology
-Inter-Satellite link
-LED-camera link
Commanded States
-Target attitude
-Target position
-Chief inertial pose
Delivered torque
Delivered force
Requested torque
Requested force
Attitude error
Position/ velocity
error
Range & angle estimates
Attitude estimate
Commanded position & attitude
Wheel Allocation
-Least squares allocation
-4 Reaction wheels
Thruster Allocation
-Convex allocation
-12 Thrusters
Thruster torque
6-DOF RK7(8) ephemeris propagation
Delivered force and torque
Delivered torque
New attitude
New relative state
Introduction
Background
Problem
Methodology
Results
Conclusion
Sensors/Commanded states
Notes: So ive convinced you that errors on the order of sub mm are of interest,so I think the next task is to convince you that my simulation can actually capture that. This is a diagram of the follower control system that I simulate.
So highlighted in the red box you can see the sensors and commanded states that the followers receive at varying rates, including a star tracker, imu, laser metrology, a camera-LED link, and an inter satellite link to receive the commanded and chief states.

## Slide 20
Follower Spacecraft Control System
Attitude Estimation
-MRP square root UKF
Attitude Control
-MRP PD feedback
Position Estimation
-CR3BP nonlinear square root EKF
Position Control
-CR3BP LQI
or
-PD
Attitude Sensors
-Star tracker
-IMU
Position Sensors
-Laser metrology
-Inter-Satellite link
-LED-camera link
Commanded States
-Target attitude
-Target position
-Chief inertial pose
Delivered torque
Delivered force
Requested torque
Requested force
Attitude error
Position/ velocity
error
Range & angle estimates
Attitude estimate
Commanded position & attitude
Wheel Allocation
-Least squares allocation
-4 Reaction wheels
Thruster Allocation
-Convex allocation
-12 Thrusters
Thruster torque
6-DOF RK7(8) ephemeris propagation
Delivered force and torque
Delivered torque
New attitude
New relative state
Introduction
Background
Problem
Methodology
Results
Conclusion
Estimation
Notes: These are passed to 2 separate Kalman filters for attitude, and relative position, and velocity estimates.

## Slide 21
Follower Spacecraft Control System
Attitude Estimation
-MRP square root UKF
Attitude Control
-MRP PD feedback
Position Estimation
-CR3BP nonlinear square root EKF
Position Control
-CR3BP LQI
or
-PD
Attitude Sensors
-Star tracker
-IMU
Position Sensors
-Laser metrology
-Inter-Satellite link
-LED-camera link
Commanded States
-Target attitude
-Target position
-Chief inertial pose
Delivered torque
Delivered force
Requested torque
Requested force
Attitude error
Position/ velocity
error
Range & angle estimates
Attitude estimate
Commanded position & attitude
Wheel Allocation
-Least squares allocation
-4 Reaction wheels
Thruster Allocation
-Convex allocation
-12 Thrusters
Thruster torque
6-DOF RK7(8) ephemeris propagation
Delivered force and torque
Delivered torque
New attitude
New relative state
Introduction
Background
Problem
Methodology
Results
Conclusion
Control
Notes: We then have the attitude and formation control blocks. The position controller is one of the trade variables, so this can either be a PD controller or the CR3BP based LQI.

## Slide 22
Follower Spacecraft Control System
Attitude Estimation
-MRP square root UKF
Attitude Control
-MRP PD feedback
Position Estimation
-CR3BP nonlinear square root EKF
Position Control
-CR3BP LQI
or
-PD
Attitude Sensors
-Star tracker
-IMU
Position Sensors
-Laser metrology
-Inter-Satellite link
-LED-camera link
Commanded States
-Target attitude
-Target position
-Chief inertial pose
Delivered torque
Delivered force
Requested torque
Requested force
Attitude error
Position/ velocity
error
Range & angle estimates
Attitude estimate
Commanded position & attitude
Wheel Allocation
-Least squares allocation
-4 Reaction wheels
Thruster Allocation
-Convex allocation
-12 Thrusters
Thruster torque
6-DOF RK7(8) ephemeris propagation
Delivered force and torque
Delivered torque
New attitude
New relative state
Introduction
Background
Problem
Methodology
Results
Conclusion
Allocation/Actuation
Notes: The requested force and torque is then sent through allocators, and models of the reaction wheels and thrusters.

## Slide 23
Follower Spacecraft Control System
Attitude Estimation
-MRP square root UKF
Attitude Control
-MRP PD feedback
Position Estimation
-CR3BP nonlinear square root EKF
Position Control
-CR3BP LQI
or
-PD
Attitude Sensors
-Star tracker
-IMU
Position Sensors
-Laser metrology
-Inter-Satellite link
-LED-camera link
Commanded States
-Target attitude
-Target position
-Chief inertial pose
Delivered torque
Delivered force
Requested torque
Requested force
Attitude error
Position/ velocity
error
Range & angle estimates
Attitude estimate
Commanded position & attitude
Wheel Allocation
-Least squares allocation
-4 Reaction wheels
Thruster Allocation
-Convex allocation
-12 Thrusters
Thruster torque
6-DOF RK7(8) ephemeris propagation
Delivered force and torque
Delivered torque
New attitude
New relative state
Introduction
Background
Problem
Methodology
Results
Conclusion
Propagation
Notes: The spacecraft state is then propagated with an RK78 integrator and JPL DE440 ephemeris files.

## Slide 24
Each surface area is assigned, normal direction, reflectivity, absorptivity, emissivity, and thermal reradiation. Forces and torques are summed per surface.
Introduction
Background
Problem
Methodology
Results
Conclusion
Notes: Here is the actual equations for force and torque propagation, which takes into account all of the relevant torques and forces.

## Slide 25
Each surface area is assigned, normal direction, reflectivity, absorptivity, emissivity, and thermal reradiation. Forces and torques are summed per surface.
Gravitational force and torque
Introduction
Background
Problem
Methodology
Results
Conclusion
Notes: This includes the gravity of the sun, earth, moon, venus, and Jupiter.

## Slide 26
Each surface area is assigned, normal direction, reflectivity, absorptivity, emissivity, and thermal reradiation. Forces and torques are summed per surface.
Gravitational force and torque
Solar radiation force and torque
Introduction
Background
Problem
Methodology
Results
Conclusion
Notes: Solar radiation pressure based on individual facet sums

## Slide 27
Each surface area is assigned, normal direction, reflectivity, absorptivity, emissivity, and thermal reradiation. Forces and torques are summed per surface.
Gravitational force and torque
Thermal reradiation force and torque
Solar radiation force and torque
Introduction
Background
Problem
Methodology
Results
Conclusion
Notes: The thermal reradiation of these facets, which some may know as the yarkovsky effect

## Slide 28
Each surface area is assigned, normal direction, reflectivity, absorptivity, emissivity, and thermal reradiation. Forces and torques are summed per surface.
Gravitational force and torque
Earth albedo and infrared light force and torque
Thermal reradiation force and torque
Solar radiation force and torque
Introduction
Background
Problem
Methodology
Results
Conclusion
Notes: And earth albedo and infrared radiation. This is propagated at a rate of 100Hz with the rk78 integrator.

## Slide 29
Inter-Satellite Sensors
Laser Metrology
LED Centroiding
Inter-Satellite Link
Introduction
Background
Problem
Methodology
Results
Conclusion
Notes: High fidelity sensor models are also fundamental to the results in this study. This includes modelling the laser metrology, led centroiding, and inter satellite link

## Slide 30
Laser Metrology
Radiometric link budget with a white noise draw that scales inversely with the square root of that received power.
Introduction
Background
Problem
Methodology
Results
Conclusion
Notes: I don’t have time to go into all the sensors, but a key driver of performance in this study is the laser metrology, so ill go a bit more in depth on how that’s simulated.
So there's 4 different noise sources that I simulate for this sensor. First is a rfull radiometric budget where white nosie scales inversely with the square root of received power.

## Slide 31
Laser Metrology
Radiometric link budget with a white noise draw that scales inversely with the square root of that received power.
Pink noise signal via a first-order autoregressive process, scaled proportionally to the distance between spacecraft.
Introduction
Background
Problem
Methodology
Results
Conclusion
Notes: There is then frequency based noise- for a given wavelength and distance, theres some minimum uncertainty that scales proportionally to the distance between spacecraft as pink noise

## Slide 32
Laser Metrology
Radiometric link budget with a white noise draw that scales inversely with the square root of that received power.
Pink noise signal via a first-order autoregressive process, scaled proportionally to the distance between spacecraft.
The Path change caused by spacecraft pointing jitter is added to a randomized linear coupling matrix representing lingering post-calibration errors.
Introduction
Background
Problem
Methodology
Results
Conclusion
Notes: There is also tilt to length coupling where if the spacecraft’s attitude is jittering, this can be directly seen by the metrology system. This can be calibrated out

## Slide 33
Laser Metrology
Radiometric link budget with a white noise draw that scales inversely with the square root of that received power.
Pink noise signal via a first-order autoregressive process, scaled proportionally to the distance between spacecraft.
The Path change caused by spacecraft pointing jitter is added to a randomized linear coupling matrix representing lingering post-calibration errors.
Simulated via a first-order Gauss-Markov random walk applied directly to the body-frame metrology head mounting vectors.
Introduction
Background
Problem
Methodology
Results
Conclusion
Notes: But given the fourth noise source, thermal drift can cause the calibration to be off.
So this hopefully gives you an idea of the level that the sensors are simulated to.

## Slide 34
Introduction
Background
Problem
Methodology
Results
Conclusion

## Slide 35
Introduction
Background
Problem
Methodology
Results
Conclusion
Controller selection sets the accuracy–propellant trade
Array-rotation period is the common Δv driver
In- vs out-of-plane affects the LQI controller only

## Slide 36
Relative Factor Sensitivity Percentages
Introduction
Background
Problem
Methodology
Results
Conclusion
Notes: So presented differently, this shows the relative sensitivity of each trade variable. you can
For delta-v, the thing that matters are the rotation rate for both controllers, and for the lqi, the chief placement matters more due to the degradation in sensor performance.

## Slide 37
GNC and optical control must be co-designed: Formation errors couple directly into optical-path difference and planet-modulation error.
Controller selection sets the accuracy–propellant trade: CR3BP–LQI achieved 1–2 mm error, but came with the cost of higher Δv; with LQI, the out-of-plane combiner adds a large Δv penalty.
Array-rotation periods are the common Δv driver: Array rotation periods raise Δv, and substantially increase LQI formation error. Pointing angle and chief-orbit family were secondary.
Introduction
Background
Problem
Methodology
Results
Conclusion
Key Takeaways
Any Questions? Aiden Weatherbee, MSc, Astronautics and Robotics Laboratory (ASTRO Lab), York University, Email: aidenweatherbee@hotmail.com
Notes: Thanks for attending my presentation. I welcome any questions

## Slide 38
References
Cockell, C. S., Léger, A., Fridlund, M., et al., "Darwin—A Mission to Detect, and Search for Life on, Extrasolar Planets," Experimental Astronomy, Vol. 23, Nos. 1–2, 2009, pp. 435–461
Lawson, P. R., et al., "Terrestrial Planet Finder Interferometer (TPF-I): Response to Astro2010 Request for Information for Proposed Activities," Jet Propulsion Laboratory, Pasadena, CA, March 2009. URL: https://www.astro.princeton.edu/~dns/FRS120/RFI/134_TPF-I_Lawson_EOS.pdf
European Space Agency, "Darwin's six telescopes," ESA Multimedia, June 2015. URL: https://www.esa.int/ESA_Multimedia/Images/2015/06/Darwin_s_six_telescopes
European Space Agency, "Proba-3," ESA Space Engineering & Technology. URL: https://www.esa.int/Enabling_Support/Space_Engineering_Technology/Proba-3
Space Rendezvous Laboratory, "STARI," Stanford University. URL: https://slab.stanford.edu/projects/stari
National Aeronautics and Space Administration, "GRACE-FO," NASA Science, November 2025. URL: https://science.nasa.gov/mission/grace-fo/
Gargaud, M., et al. (eds), Encyclopedia of Astrobiology, Springer, Berlin, Heidelberg. DOI: 10.1007/978-3-642-27833-4_1088-3. URL: https://link.springer.com/rwe/10.1007/978-3-642-27833-4_1088-3